## Slide 1: Title Lorem Ipsum
Sit Dolor Amet

## Slide 2: Title Lorem Ipsum
Lorem Ipsum
Dolor Sit Amet
Lorem Ipsum
Dolor Sit Amet
Lorem Ipsum
Dolor Sit Amet
Consectetuer Elit
Nunc Viverra
Consectetuer Elit
Nunc Viverra
Consectetuer Elit
Nunc Viverra

## Slide 5
General board control
import pyb
pyb.repl_uart(pyb.UART(3, 9600, timeout_char=1000)) # duplicate REPL on UART(3)
pyb.wfi() # pause CPU, waiting for interrupt
pyb.stop() # stop CPU, waiting for external interrupt

## Slide 6
Delay and timing
Use the time module:
import utime
time.sleep(1) # sleep for 1 second
time.sleep_ms(500) # sleep for 500 milliseconds
time.sleep_us(10) # sleep for 10 microseconds
start = time.ticks_ms() # get value of millisecond counter
delta = time.ticks_diff(time.ticks_ms(), start) # compute time difference

## Slide 7
LEDs
from pyb import LED
led = LED(1) # red led
led.toggle()
led.on()
led.off()
LED Pinout:
LED(1) -> Red RGB LED Segment
LED(2) -> Green RGB LED Segment
LED(3) -> Blue RGB LED Segment
LED(4) -> IR LEDs

## Slide 8
Pins and GPIO
from pyb import Pin
p_out = Pin('P7', Pin.OUT_PP)
p_out.high()
p_out.low()
p_in = Pin('P8', Pin.IN, Pin.PULL_UP)
p_in.value() # get value, 0 or 1
GPIO Pinout:
Pin(‘P0’) -> P0 (PB15)
Pin(‘P1’) -> P1 (PB14)
Pin(‘P2’) -> P2 (PB13)
Pin(‘P3’) -> P3 (PB12)
Pin(‘P4’) -> P4 (PB10)
Pin(‘P5’) -> P5 (PB11)
Pin(‘P6’) -> P6 (PA5)
Pin(‘P7’) -> P7 (PD12)
Pin(‘P8’) -> P8 (PD13)
Pin(‘P9’) -> P9 (PD14) (OpenMV Cam M7/H7 Only)
All pins are 5V tolerant with a 3.3V output (P6 is not 5V tolerant in ADC or DAC mode).
All pins can sink or source up to 25 mA (Up to 120 mA in total between all pins).

## Slide 9
Servo control
from pyb import Servo
s1 = Servo(1) # servo on position 1 (P7)
s1.angle(45) # move to 45 degrees
s1.angle(-60, 1500) # move to -60 degrees in 1500ms
s1.speed(50) # for continuous rotation servos
Servo Pinout:
Servo(1) -> P7 (PD12)
Servo(2) -> P8 (PD13)
Servo(3) -> P9 (PD14) (OpenMV Cam M7/H7 Only - Not OpenMV Cam H7 Plus)

## Slide 10
External interrupts
from pyb import Pin, ExtInt
callback = lambda e: print("intr")
ext = ExtInt(Pin('P7'), ExtInt.IRQ_RISING, Pin.PULL_NONE, callback)
GPIO Pinout:
Pin(‘P0’) -> P0 (PB15)
Pin(‘P1’) -> P1 (PB14)
Pin(‘P2’) -> P2 (PB13)
Pin(‘P3’) -> P3 (PB12)
Pin(‘P4’) -> P4 (PB10)
Pin(‘P5’) -> P5 (PB11)
Pin(‘P6’) -> P6 (PA5)
Pin(‘P7’) -> P7 (PD12)
Pin(‘P8’) -> P8 (PD13)
Pin(‘P9’) -> P9 (PD14) (OpenMV Cam M7/H7 Only)

## Slide 11
Timers
See pyb.Timer.
from pyb import Timer
tim = Timer(2, freq=1000)
tim.counter() # get counter value
tim.freq(0.5) # 0.5 Hz
tim.callback(lambda t: pyb.LED(1).toggle())
For OpenMV Cam M4: TIM2, TIM3, and TIM4
For OpenMV Cam F7: TIM2, TIM3, TIM4 and TIM7 through TIM14
For OpenMV Cam H7: TIM2, TIM3, TIM4, TIM7, TIM8 and TIM12 through TIM17
Timer Pinout:
Timer 1 Channel 3 Negative -> P0 (PB15)
Timer 1 Channel 2 Negative -> P1 (PB14)
Timer 1 Channel 1 Negative -> P2 (PB13)
Timer 2 Channel 3 Positive -> P4 (PB10)
Timer 2 Channel 4 Positive -> P5 (PB11)
Timer 2 Channel 1 Positive -> P6 (PA5)
Timer 4 Channel 1 Negative -> P7 (PD12)
Timer 4 Channel 2 Negative -> P8 (PD13)
Timer 4 Channel 3 Positive -> P9 (PD14) (OpenMV Cam M7/H7 Only - Not OpenMV Cam H7 Plus)

## Slide 12
PWM (pulse width modulation)
See pyb.Pin and pyb.Timer.
from pyb import Pin, Timer
p = Pin('P4') # P4 has TIM2, CH3
tim = Timer(2, freq=1000)
ch = tim.channel(3, Timer.PWM, pin=p)
ch.pulse_width_percent(50)
For OpenMV Cam M4: TIM2, TIM3, and TIM4
For OpenMV Cam F7: TIM2, TIM3, TIM4 and TIM7 through TIM14
For OpenMV Cam H7: TIM2, TIM3, TIM4, TIM7, TIM8 and TIM12 through TIM17
Timer Pinout:
Timer 1 Channel 3 Negative -> P0 (PB15)
Timer 1 Channel 2 Negative -> P1 (PB14)
Timer 1 Channel 1 Negative -> P2 (PB13)
Timer 2 Channel 3 Positive -> P4 (PB10)
Timer 2 Channel 4 Positive -> P5 (PB11)
Timer 2 Channel 1 Positive -> P6 (PA5)
Timer 4 Channel 1 Negative -> P7 (PD12)
Timer 4 Channel 2 Negative -> P8 (PD13)
Timer 4 Channel 3 Positive -> P9 (PD14) (OpenMV Cam M7/H7 Only - Not OpenMV Cam H7 Plus)

## Slide 13
ADC (analog to digital conversion)
from pyb import Pin, ADC
adc = ADC(Pin('P6'))
adc.read() # read value, 0-4095
P6 is 3.3V tolerant in ADC mode - NOT 5V TOLERANT!

## Slide 14
DAC (digital to analog conversion)
from pyb import Pin, DAC
dac = DAC('P6')
dac.write(120) # output between 0 and 255
P6 is 3.3V tolerant in ADC mode - NOT 5V TOLERANT!

## Slide 15
Serial BUS
UART
uart = UART(3, 9600, timeout_char=1000)
uart.write('hello')
uart.read(5) # read up to 5 bytes
UART Pinout:
UART 3 RX -> P5 (PB11)
UART 3 TX -> P4 (PB10)
UART 1 RX -> P0 (PB15) (OpenMV Cam M7/H7 Only)
UART 1 TX -> P1 (PB14) (OpenMV Cam M7/H7 Only)

## Slide 16
Serial BUS
SPI bus
from pyb import SPI
spi = SPI(2, SPI.MASTER, baudrate=1000000, polarity=1, phase=0)
spi.send('hello')
spi.recv(5) # receive 5 bytes on the bus
spi.send_recv('hello') # send a receive 5 bytes
SPI Pinout:
SPI 2 MOSI (Master-Out-Slave-In) -> P0 (PB15)
SPI 2 MISO (Master-In-Slave-Out) -> P1 (PB14)
SPI 2 SCLK (Serial Clock) -> P2 (PB13)
SPI 2 SS (Serial Select) -> P3 (PB12)

## Slide 17
Serial BUS
I2C bus
from pyb import I2C
i2c = I2C(2, I2C.MASTER, baudrate=100000)
i2c.scan() # returns list of slave addresses
i2c.send('hello', 0x42) # send 5 bytes to slave with address 0x42
i2c.recv(5, 0x42) # receive 5 bytes from slave
i2c.mem_read(2, 0x42, 0x10) # read 2 bytes from slave 0x42, slave memory 0x10
i2c.mem_write('xy', 0x42, 0x10) # write 2 bytes to slave 0x42, slave memory 0x10
I2C Pinout:
I2C 2 SCL (Serial Clock) -> P4 (PB10)
I2C 2 SDA (Serial Data) -> P5 (PB11)
I2C 4 SCL (Serial Clock) -> P7 (PD13) (OpenMV Cam M7/H7 Only)
I2C 4 SDA (Serial Data) -> P8 (PD12) (OpenMV Cam M7/H7 Only)